## Slide 1: Nuclear Power: Status, Issues and Prospects James F. Jackson

## Slide 2: Nuclear Power Advantages
Carbon free base-load (24/7) power—reliable and expandable
Centuries of domestic fuel — no mining for 100 yrs using advanced fuel cycle
Very small fuel and waste volumes

## Slide 3: Nuclear Power Challenges
High capital costs and long construction times ( ≈ $12 B and 9 years for Plant Vogtle)
Radioactive waste disposal
Concern over serious accidents like TMI
Reactors and nuclear weapons involve similar materials (non-proliferation)

## Slide 4: Status of Nuclear Power
445 plants worldwide-- ≈10% of electricity
93 plants in U.S.-- ≈20% of electricity (license extensions completed on almost all)
50 new plants under construction worldwide, but only 2 are in the U.S. (China has 12)
≈ 30 plants cancelled in U.S. due to costs and cheap natural gas
Strong interest in small modular reactors (SMRs) to address cost and safety issues

## Slide 5: U.S. Nuclear Plants

## Slide 6: Pressurized Water Reactor

## Slide 7: Boiling Water Reactor

## Slide 8: Vogtle Plant: 2 Unit PWR

## Slide 9: Vogtle Plant: Proposed Addition

## Slide 10: Vogtle Plant: AP 1000 (2021)

## Slide 11: Current U.S. Fuel Cycle

## Slide 12
Yellowcake, U3O8 , is packaged into 55-gallon drums
at a uranium mill, and then shipped to a conversion plant

## Slide 13: Uranium Conversion
Only operating U.S. plant in Metropolis, IL
Converts U3O8 (yellowcake) to UF6
UF6 sublimes at 1340F
Packaged into 10 to 14 ton cylinders
Allowed to cool 5 days to solidify
Shipped to enrichment plant

## Slide 14
Natural uranium consists of three isotopes:
Isotope % Abundance Half Life (years)
238U 99.284 4.5 billion
235U* 0.711 704 million
234U 0.005 245 thousand
Properties of Natural Uranium
*Must be enriched up to about 3-5% for commercial fuel

## Slide 15: Gaseous Diffusion Enrichment
Flow of UF6 through a single stage

## Slide 16
Oak Ridge Gaseous Diffusion Plant
K-25 Plant, Oak Ridge, in decommissioning since 1985
Notes: Oak Ridge

## Slide 17
U Enrichment by
Gas Centrifuge

## Slide 18: Views of a Urenco Gas Centrifuge Cascade

## Slide 19: Laser Enrichment
Science developed in 70s at Los Alamos and Livermore Labs
Very high separation rates at each stage (not dependent on tiny U235/U238 mass difference)
Atomic Vapor (AVLIS)
Molecular UF6 (MLIS)
Molecular UF6 (SILEX)

## Slide 20: Westinghouse Fuel Fabrication Facility, South Carolina

## Slide 21
UO2 pellets are about 0.5 in.
in length & 0.33 in.
in diameter.
They are "dished" slightly on each end to allow for thermal expansion.
Pellet Production

## Slide 22: Fuel Rods Filled With Pellets Are Grouped Into Fuel Assemblies
Notes: The pellets are sealed in metal fuel rods, 12 feet long and half an inch in diameter. Fuel rods are made of zirconium, which resists heat, radiation and corrosion. The rods are bundled together into fuel assemblies, which are placed inside the reactor.

## Slide 25: PWR Pressurizer

## Slide 27: Nuclear Reactor Safety
Public fear of major accidents is one barrier to the expansion of nuclear power
Key issue: avoid any large releases of radioactive materials
Engineering challenge: never allow fuel rods to melt
  Mobilizes radioactive nuclides and produces hydrogen
Approach: Use passive and active safety systems to shut down the chain reaction and remove radioactive decay heat (long term)

## Slide 28
Uranium Fission Process

## Slide 29: Large Break Loss of Coolant

## Slide 30: Three Mile Island Plant

## Slide 31: Engineering Lessons Learned
Defense in depth critical – passive vs. active safeguards
Man-machine interface critical
Operators must be well trained to deal with a wide range of accident conditions
No substitute for operational experience
Need strong maintenance, inspections and lessons learned programs

## Slide 32: Strong Record of Safe Operation
Improved operator training, facility maintenance, formality of operations, and lessons-learned programs since Three-Mile-Island accident
Strong oversight by the Nuclear Regulatory Commission
Precursor events dramatically reduced:
1985: 2.37 per reactor-year
1998: 0.04 per reactor-year
40 years of safe and reliable operation in U.S

## Slide 33: Fukushima Japan Nuclear Site Four BWR Units

## Slide 34: BWR Containment Structure

## Slide 35: Fukushima Accident (March 11, 2011
Large earthquake leads to reactors shutting down and activating emergency systems
45 foot tsunami hits plants designed to tolerate a 18 foot tsunami
Plants lose all offsite and diesel backup power needed for emergency cooling pumps
Fuel rods melt in three reactors and one fuel storage pool, producing hydrogen
Hydrogen explosions severely damage the outer reactor structures

## Slide 36: Fukushima Accident (contd.)
Damaged core material remains in reactor vessels
Radioactive material released, mostly in water that flowed into the ocean
Long term cooling eventually established
Projections indicate no one will be harmed by the released radioactive material, but people temporarily evacuated as a precausion

## Slide 37: Fukushima Plants Post Accident

## Slide 38: Impact of Fukushima Accident
Countries with a strong commitment to nuclear continued their plans (except Japan)
Some others, like Germany are planning to phase out their nuclear plants
All countries reviewed the lessons learned and ensured that external risks, such as earthquakes, were properly evaluated
Polls in U.S. indicate ongoing 50/50 support for nuclear (higher near existing plants)

## Slide 39: “Yeah, but what about the waste?”
Near Term: Store used nuclear fuel assemblies
  Interim storage at plants
  Geologic storage (DOE responsible)
Long Term: Essentially “burn” all actinides using an advanced fuel cycle, and only store fission products
  Dramatically reduces waste volume and toxicity
  Extracts all energy from uranium resources

## Slide 40
Uranium Fission Process

## Slide 41: Nuclear Power Plants Produce Plutonium
Neutron U-238 Pu-239
Pu-239 fissions just like U-235
Pu-239 can then be used as a nuclear fuel, or in the production of nuclear weapons

## Slide 45: Reactor Site Storage Cask

## Slide 46: Comparative Size of Targets
WTC 208’ wide 1,353’ tall
Pentagon 1,489’ wide (921’ per side) 71’ tall
Spent Fuel Pool 80’ wide 40’ tall
Containment Building 130’ wide 160’ tall
Dry Casks 10’ wide 20’ tall (12 depicted)

## Slide 47: Yucca Mountain Site

## Slide 48: Yucca Mountain Site

## Slide 50: Shipping Cask

## Slide 51: Shipping Cask Test with 80mph Locomotive

## Slide 52: Locomotive Impacting the Shipping Cask

## Slide 53: Shipping Cask after Test

## Slide 54: Spent Fuel Storage Canister

## Slide 55: Engineered and Natural Barriers

## Slide 60: Yucca Mountain Calculated Doses from the DOE SAR
Max Annual Mean Dose during the first 10,000 years after closure: 0.24 mrem
Max Annual Median Dose during the first 1,000,000 years after closure: 0.96 mrem.
This max dose occurs at about 720,000 years after closure.

## Slide 61: Current Status in the U.S.
Yucca Mountain project killed politically
Interim storage at reactor sites in dry casks (endorsed by the NRC)
By law, the DOE is still responsible for taking ownership and disposing of spent fuel
Still unsettled and very political

## Slide 64
Depleted Uranium – Enrichment Tailings

## Slide 65: Complete Fuel Cycle

## Slide 66: Toxicity of Used Nuclear Fuel Constituents

## Slide 70: Advanced Fuel Cycle

## Slide 72: Nuclear Waste, Fuel Cycle and Reactor Options
Long-term viability requires fuel recycle to extend fuel resources and reduce waste volume and toxicity
Will still need a Yucca Mountain type repository to store wastes
Factory-built Small Modular Reactors with walk away safety hold real promise

## Slide 73: Natural Risks (WASH 1400)

## Slide 74: Man-Caused Risks (WASH 1400)